## Slide 1: 進捗報告 Progress report
Tomoyuki Ueda
芝浦工業大学
宮田研究室

## Slide 2: 実験方法
トラヒック負荷ごとに検知
  2.4GHz帯で実験
  Iperf やデバイスを使用した負荷
  Iperfなしと3MB, 5MB, 7MBの負荷
Detection with separate traffic load
Experimental method
  Experiments in the 2.4GHz band
  Load with Iperf and devices
ping
RTT取得
Get RTT
Iperfの負荷
Load using iperf
Without Iperf and 3MB, 5MB and 7MB load
google.com
Notes: udpのパケットを送信

## Slide 3: 取得結果
Iperfなし・PC3台+iPhone1台に接続
Acquisition Result
Without iperf, connect with 3 PCs and an iPhone.
Chart: Time [ms]
Buffalo→正規AP aterm→不正AP
Legitimate
Rogue

## Slide 4: 取得結果
Chart: Time [ms]
3MBの負荷・PC3台+iPhone1台に接続
Acquisition Result
Load 3MB, connect with 3 PCs and an iPhone.
Buffalo→正規AP aterm→不正AP
Legitimate
Rogue

## Slide 5: 取得結果
Chart: Time [ms]
5MBの負荷・PC3台+iPhone1台に接続
Acquisition Result
Load 5MB, connect with 3 PCs and an iPhone.
Buffalo→正規AP aterm→不正AP
Legitimate
Rogue

## Slide 6: 取得結果
Chart: Time [ms]
7MBの負荷・PC3台+iPhone1台に接続
Acquisition Result
Load 7MB, connect with 3 PCs and an iPhone.
Buffalo→正規AP aterm→不正AP
Rogue
Legitimate

## Slide 7
平均、分散ともに正規＜不正
負荷が上がるにつれRTT上昇
検知プログラムの修正・適用 (途中)
Both mean and variance are legitimate < rogue
まとめと課題
Summary and Issues
RTT increases as load increases
Correction and application of detection programs
 | baffalo | aterm
variance | 23.2343 | 558.655
average | 7.729097 | 20.25342
 | baffalo | aterm
variance | 115.3089 | 1533.754
average | 10.70608 | 35.24823
 | baffalo | aterm
variance | 153.7201 | 2105.33
average | 12.59797 | 42.54448
 | baffalo | aterm
variance | 502.101 | 4069.698
average | 19.08844 | 57.70722
0MB
3MB
5MB
7MB