## Slide 1: 進捗報告 Progress report
Tomoyuki Ueda
芝浦工業大学
宮田研究室

## Slide 2: Self introduction
Name : Tomoyuki Ueda
Age : 22
Birthplace : Tokyo
Favorite, hobby : Ramen, Work out frequently
Notes: I'll start with a self-introduction. My name is (name). I'm from Tokyo and currently 22 years old.
As for my hobbies and interests, I enjoy eating ramen and working out frequently.
I'm not very good at speaking English, but nice to meet you

## Slide 3: Research Interests
Theme : Evil-Twin Attack detection
  Spoof legitimate wireless LAN access points and launch various attacks against connected users.
Conventional Issues :
Detection errors under high traffic load
Rogue AP
Legitimate AP
user
SSID : Free-1
？
SSID : Free-1
Notes: Next, I'll explain my research topic. I'm researching on detecting evil twin attacks.
Evil twin attacks are spoof legitimate wireless LAN access points and launch various attacks against connected users.
However, there was a problem that detection errors were more likely to occur when the traffic load was high.

## Slide 4: Experimental method
Detection with separate traffic load
  Experiments in the 2.4GHz band
  Load with Iperf and devices
  Without Iperf and 3MB, 5MB and 7MB load
ping
Get RTT
Load using iperf
google.com
Notes: I considered setting a threshold for each traffic load and detection.
We used iperf between the 2 generations of pc's and pinged google.com in that state, and experimented with the RTT until the ping was returned.
The results are shown in the next slide.

## Slide 5: Detection method (1)
Using the k-means method
  There are two groups to divide
  Applies to normal/attack data that is split
  Find the y-axis ratio of the coordinates of the center of gravity point
RTT [ms]
Number of packets
Notes: The detection method is described below. The k-means method is used for detection.
This is a method that groups data into a defined number This method is applied to data divided into several groups.
The number of center-of-gravity points and the number of divided groups are two, and the ratio of the y-coordinates of the coordinates of the center-of-gravity points of these two points is calculated.

## Slide 6: Detection method (2)
Calculate y-axis ratio of center of gravity point from normal data ➡ Threshold value
Legitimate APs
  The y-axis ratio calculated from the normal data
Rougue APs
  The y-axis ratio calculated from the attack data
RTT [ms]
RTT [ms]
Data number
Greater than threshold
➡There is rogue AP
Data number
Notes: This k-means method is used to determine the y-axis ratio of the coordinates of the center of gravity point to the RTT data during normal and attack.
The y-axis ratio calculated from the RTT data under normal conditions is used as the threshold value.
The y-axis ratio of the coordinates of the centre of gravity points during normal and attack is then compared with a threshold value; if the y-axis ratio is greater than the threshold value, an illegal AP is determined to exist.

## Slide 7: 取得結果
Without iperf, connect with 3 PCs and an iPhone.
Acquisition Result
Chart: Time [ms]
Buffalo→Legitimate aterm→Rogue
Notes: This is the result when done without iperf.

## Slide 8: 取得結果
Chart: Time [ms]
Load 3MB, connect with 3 PCs and an iPhone.
Acquisition Result
Buffalo→Legitimate aterm→Rogue
Notes: This is the result of a 3 MB load on iperf.

## Slide 9: 取得結果
Chart: Time [ms]
Load 5MB, connect with 3 PCs and an iPhone.
Acquisition Result
Buffalo→Legitimate aterm→Rogue
Notes: This is the result of a 5 MB load on iperf.

## Slide 10: 取得結果
Chart: Time [ms]
Load 7MB, connect with 3 PCs and an iPhone.
Acquisition Result
Buffalo→Legitimate aterm→Rogue
Notes: This is the result of a 7 MB load on iperf.
Threshold values are set for each of these RTT data for detection.

## Slide 11
平均、分散ともに正規＜不正
負荷が上がるにつれRTT上昇
検知プログラムの適用
Both mean and variance are legitimate < rogue
取得結果
RTT increases as load increases
Application of detection programs
 | baffalo | aterm
variance | 23.2343 | 558.655
average | 7.729097 | 20.25342
 | baffalo | aterm
variance | 115.3089 | 1533.754
average | 10.70608 | 35.24823
 | baffalo | aterm
variance | 153.7201 | 2105.33
average | 12.59797 | 42.54448
 | baffalo | aterm
variance | 502.101 | 4069.698
average | 19.08844 | 57.70722
0MB
3MB
5MB
7MB
Acquisition Result
Notes: This is the mean and variance in each pattern.

## Slide 12: 検知結果(提案手法)
F値：0.92，正解率：0.92
1回あたり300パケットで4回測定
  1回を訓練データ、3回をテストデータに使用
 | Iperf なし |  |  | Iperf 3MB |  |  | Iperf 5MB |  |  | Iperf 7MB |  | 
正規AP | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | × | 〇 | ×
不正AP | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇
Detection results (proposed method)
F-score : 0.92, Accuracy : 0.92
Legitimate
Not using iperf
Rogue
Iperf 3MB
Iperf 5MB
Iperf 7MB
Four measurements with 300 packets per measurement
1 time used for training data, 3 times for test data

## Slide 13: 検知結果(対抗手法)
F値：0.74，正解率：0.79
Iperfなしの時の閾値で検知
 | Iperf なし |  |  | Iperf 3MB |  |  | Iperf 5MB |  |  | Iperf 7MB |  | 
正規AP | 〇 | 〇 | 〇 | 〇 | 〇 | × | × | 〇 | 〇 | × | × | ×
不正AP | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇
F-score : 0.92, Accuracy : 0.92
Legitimate
Not using iperf
Rogue
Iperf 3MB
Iperf 5MB
Iperf 7MB
Detection at threshold without Iperf
Detection results (competing method)

## Slide 14: IoT機器なしでの実験
iperfの7MB程度の負荷でパケットロス大
  IoT機器だけですでに負荷が高い可能性
  IoT機器を除いての測定
Packet loss is high with a load of about 7 MB of iperf.
Experiment under no IoT devices
Possibly already overloaded with IoT devices alone.
Measurements excluding IoT devices
Notes: With IoT devices connected, packet loss was significant with a load of around 7MB of iperf.
Therefore, considering the already high load potential of the IoT alone, we decided to measure the data even with the IoT devices disconnected.

## Slide 15: IoT機器なしでの実験（結果）
ロスなしだと15MBの負荷まで可能
Iperfなし・7MB・15MBで実験
Chart: Time
Without packet loss, loads of up to 15 MB can be measured.
Experiments with no Iperf, 7MB and 15MB
Experiment under no IoT devices
Notes: At the limit of no packet loss, it was possible to measure loads up to about 15 MB.
Packet loss was observed above 15 MB.
Measurements were taken with no Iperf, 7MB and 15MB.

## Slide 16: IoTありとなしの比較
←IoT接続時 Non-iperf・7MB
←IoT非接続時
Non-iperf・7MB
Chart: Time [ms]
Chart: Time
 | 0MB | 7MB
variance | 60.27545 | 235.8639
average | 9.761745 | 15.34014
 | 0MB | 7MB
average | 6.814815 | 12.27703
variance | 17.8546 | 55.22055
Comparison with and without IoT
When connected to IoT
When IoT is not connected

## Slide 17: まとめと予定 Summary and plans
IoTの負荷の影響の確認ができた
IoTなしでのRTTを取得完了（今は途中）
IoTを含まないRTTを使用した検知
The impact of the IoT load could be checked.
Completed getting RTT without IoT (now on the way)
Detection using RTT without IoT.