## Slide 1: 進捗報告 Progress report
Tomoyuki Ueda
芝浦工業大学
宮田研究室

## Slide 2: Research background & objective
Theme : Evil-Twin Attack detection
  Spoof legitimate wireless LAN access points and launch various attacks against connected users.
Rogue AP
Legitimate AP
user
SSID : Free-1
？
SSID : Free-1
Improved accuracy of rogue AP detection
Notes: My research is to detect Evil-Twin attack.
ET is ~.

## Slide 3: Conventional methods & issue
RTT-based detection methods
  Use RTT differences between different hop counts.
  Detection by comparing the difference between the threshold and the RTT.
Rogue AP
（evil-twin）
User
Internet
Legal AP
1-hop
2-hop
RTT dispersion during congestion less considered
Notes: This is conventional method and assumed situation.
Conventional method is using RTT diffaerences ~.
However, convention methods didn’t consider RTT dispersion ~.

## Slide 4: Key idea & experimental environment
Detection with separate traffic load
  Experiments in the 2.4GHz band
  Without Iperf and 3MB, 5MB and 7MB load
16 IoT devices
Legal AP
Rogue AP
PC 1
(To measure)
PC 2
Devices
Load using iperf
between PC1 to PC2
Send ping
PC1 to google.com
google.com
Notes: Next, I discuss the experimental setup in more detail.
As mentioned earlier, we conducted the experiments using Iperf between two PCs while sending pings to google.com to measure the RTT until the ping response is received.
During the experiments, the devices connected to the AP included 3 PCs, 1 smartphone, and 16 IoT devices, and the operating frequency was set to 2.4GHz.
We performed the experiments under four traffic load conditions: no Iperf load, Iperf load of 3MB, Iperf load of 5MB, and Iperf load of 7MB.
次に、実験方法について詳しい話をします。 先ほども話した通り、2つのpc間でiperfを使い、その状態でgoogle.comにpingを打ち、pingが返ってくるまでの時間をRTTとして実験をします。 この時、APに接続しているデバイスは、3つのPCと1つのスマートフォン、16個のIoT機器であり、使用している帯域は2.4GHZで行った。 また4つのトラヒックの状態は、iperfなしの状態とiperfで3MBの負荷、5MBの負荷、7MBの負荷の状態の4つである。

## Slide 5: Experiment flow
Measure RTT
Detect with k-means
”There is rogue AP”
No
Yes
Use CDF
Done
RTT [ms]
Data number
User
AP
Get RTT
Thresholds are assigned for each traffic load

## Slide 6: Evaluation method
F-score/F-measure
  The percentage of cases predicted as rogue APs that turned out to be rogue APs.
  ➡ Precision(P)
  The rate at which rogue APs were correctly predicted as rogue APs.
  ➡ Recall(R)
  The harmonic mean of P and R ( )
Notes: The evaluation is done by F-score.
F-score is The harmonic mean of P and R.
Where P is the percentage of cases predicted as rogue APs that turned out to be rogue aps and R is The rate at which rogue APs were correctly predicted as rogue APs.

## Slide 7: Detection results (proposed method)
F-score : 0.92, Accuracy : 0.92
Four measurements with 300 packets per measurement
  1 time used for training data, 3 times for test data
 | Not using iperf |  |  | Iperf 3MB |  |  | Iperf 5MB |  |  | Iperf 7MB |  | 
Legal | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | × | 〇 | ×
Rogue | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇
Notes: In this experiment, the number of RTT data used in one experiment was 300; four measurements were made, one of which was used as the threshold.
First, let's start with the results of the proposed method.
This resulted in an F-score of 0.92 and a percentage of accuracy of 0.92.
１回の実験で使用されたRTTデータ数は300である。4回測定し、そのうち1回を閾値に利用した。

## Slide 8: Progress report
Research the Impact of the IoT
  Packet loss is large with only 7MB of iperf load
  Possibly already overloaded with IoT alone
Comparison in the following situations to confirm the impact
  Connected to 3 PCs and 1 iphone (no IoT used)
  Connect to IoT only
  Connected to IoT + 3 PCs and 1 iphone
Notes: This is why I had stopped the iperf load at 7MB
And I considered the possibility that IoT devices alone are already overloaded.

## Slide 9: Result
Connected to 3 PCs and 1 iphone (no IoT used)
Chart: Packet number

## Slide 10: Result
Connect to IoT only
Chart: Packet number

## Slide 11: Result
Connected to IoT + 3 PCs and 1 iphone

## Slide 12: Result
Average & Variance
 | average | variance
Not using iperf | 6.814815 | 17.8546
iperf 7MB | 12.27703 | 55.22055
Connected to 3 PCs and 1 iphone (no IoT used)
 | average | variance
Not using iperf | 8.19 | 9.11
iperf 7MB | 14.02 | 298.65
Connect to IoT only

## Slide 13: Result under no IoT devices
Without packet loss, loads of up to 15 MB can be measured
Experiments with no Iperf, 7MB and 15MB
Chart: Time
Notes: At the limit of no packet loss, it was possible to measure loads up to about 15 MB.
Packet loss was observed above 15 MB.
Measurements were taken with no Iperf, 7MB and 15MB.

## Slide 14: IoTありとなしの比較
←IoT接続時 Non-iperf・7MB
←IoT非接続時
Non-iperf・7MB
Chart: Time [ms]
Chart: Time
 | Iperfなし | 7MB
variance | 60.27545 | 235.8639
average | 9.761745 | 15.34014
 | Iperfなし | 7MB
average | 6.814815 | 12.27703
variance | 17.8546 | 55.22055
Comparison with and without IoT
When connected to IoT
When IoT is not connected

## Slide 15: まとめと予定 Summary and plans
IoTの負荷の影響の確認ができた
IoTなしでのRTTを取得完了（今は途中）
IoTを含まないRTTを使用した検知
The impact of the IoT load could be checked.
Completed getting RTT without IoT (now on the way)
Detection using RTT without IoT.