## Slide 1: A Client-Side Evil-Twin Attack Detection System with Threshold Considering Traffic Load
Tomoyuki Ueda, Sumiko Miyata
† Amgad Saif
† † Masataka Nakahara, † † Ayumu Kubota
Shibaura Institute of Technology
† KTH Royal Institute of Technology
† † KDDI Research
Notes: I will be presenting my research titled ”A Client-Side Evil-Twin Attack Detection System with Threshold Considering Traffic Load”

## Slide 2: Research background and objectives
Increase in access points (APs) following the Corona disaster
Increased damage caused by rogue APs
➡ Evil Twin Attack
[S. Kitisriworapan +, EURASIP Journal on Wireless Communications and Networking, 2020]
[K. C. Patel+, INDIACom, 2022]
Improved accuracy of rogue AP detection
Notes: In recent years, the number of access points (APs), commonly known as Free-WiFi, in wireless LANs has been increasing.
Additionally, with the COVID-19 pandemic, remote learning and work have become more prevalent, leading to an increase in people working remotely at cafes and restaurants. As a result, the number of APs is expected to continue to rise.
However, alongside this growth, there has been an increase in attacks known as rogue APs, such as evil-twin attacks.
Therefore, there is a demand for improving the accuracy of detecting rogue APs.

## Slide 3: Research background and objectives
Evil Twin Attack
To spoof legal wireless LAN APs and launch various attacks against connected users.
[En-Chun Kuo+, IEEE ICACT, 2018]
Rogue AP
Legal AP
User
SSID : Free-1
？
SSID : Free-1
Notes: Evil-Twin attack is a type of attack where the attacker impersonates a legal wireless LAN access point (AP) and launches various attacks against connected users.
In the example below, the rogue AP is configured with the name "Free-1," which is the same as the SSID of the legal AP.
The intention is to confuse users and trick them into connecting to the rogue AP, through which the attacker can steal personal information or deliver malware.

## Slide 4: Existing Methods
Classification of existing methods
  Fingerprint (Administrator's side)
  ➡ Features : Stable accuracy, High cost, Great hassle
  [Qiaolin Pu+, IEEE Transactions on Vehicular Technology, 2021]
  RTT : Round trip time (User side)
  ➡ Features : Low cost, Less hassle, Affected by the environment
  [S. Kitisriworapan +, EURASIP Journal on Wireless Communications and Networking, 2020]
Notes: Next, let's introduce the existing methods. Existing methods are mainly divided into two categories: those focused on detection from the administrator's side and those focused on detection from the user's side.
One of the typical methods from the administrator's side is using fingerprints. The advantage of this method is its stable detection accuracy, but the drawback is the significant cost and effort required for implementation.
On the other hand, one of the representative methods from the user's side is using Round-Trip Time (RTT). The benefit of this approach is its relatively low cost and ease of implementation, but it can be more susceptible to environmental influences.
In light of these findings, we propose a detection method that combines both RTT and fingerprinting techniques.
By integrating the advantages of both approaches, we aim to enhance the accuracy and robustness of the detection process.

## Slide 5: Assumed environment/Existing methods
RTT-based detection methods
  Leverage RTT differences between different hop counts
  Detection by comparing the difference between the threshold and the RTT.
Rogue AP
（evil-twin）
User
Internet
Legal AP
1-hop
2-hop
Notes: Let me explain the detection method using RTT. Typically, the relationship between the user, legal AP, and rogue AP is as depicted in the diagram below.
When connected to the legal AP, there is 1-hop. However, when connected to the rogue AP, there are 2-hops. As a result, the RTT tends to be longer for the two-hop scenario due to the processing and transmission time at the rogue AP.
In RTT-based detection, a threshold for RTT is determined, and if the RTT exceeds this threshold, it is considered as an indication of the presence of a rogue AP.

## Slide 6: Conventional methods and issues
RTT-based detection methods
  RTT dispersion during congestion less considered
    Improved detection accuracy by considering
  Methods using MCS (transmission rate)
    MCS： Modulation and Coding Scheme
    Getting MCS is not easy for ordinary people
    [Kitisriworapan+，J Wireless Com Network 2020，2020]
Evil-Twin detection considering traffic load
Notes: As mentioned earlier, the RTT-based detection method is susceptible to environmental influences, especially during times of traffic congestion, where the consideration of RTT dispersion is limited. The increased dispersion can lead to false detections.
Indeed, some methods have utilized the MCS index, which includes settings related to modulation and coding.
However, obtaining the MCS values is not straightforward for the general public.
Therefore, we focus on developing a new Evil-Twin detection method that takes traffic load into account.

## Slide 7: Key idea
Detection with separate traffic load
  Load with Iperf and some devices
  4 different types of loads
ping
Get RTT
Load using iperf
google.com
Some devices
PC
PC
AP
Notes: The key idea is to perform detection for each traffic load. The experiment was conducted with four different loads using Iperf and several devices.
We applied load between two PCs using Iperf while simultaneously sending pings to Google to measure the RTT.
The detailed experimental procedure will be explained later.

## Slide 8: Key idea
Detection with separate traffic load
  Load with Iperf and some devices
  4 different types of loads
ping
Get RTT
Load using iperf
google.com
PC
PC
AP
Some devices
Notes: The key idea is to perform detection for each traffic load. The experiment was conducted with four different loads using Iperf and several devices.
We applied load between two PCs using Iperf while simultaneously sending pings to Google to measure the RTT.
The detailed experimental procedure will be explained later.

## Slide 9: Proposed and competing methods
Proposed methods
  Calculation of thresholds by traffic load
  4 types of thresholds
Competing methods
  Thresholds determined in an environment without iperf
  Only one type of threshold is fixed
Notes: The competing method, as described earlier, adopts a single threshold for detection, regardless of the traffic load state.
Unlike the proposed method, which sets different thresholds for the four traffic load conditions, the competing method relies on a single threshold to determine if an Evil-Twin attack is present.

## Slide 10: Detection method (1)
Using the k-means method
  There are two groups to divide
  Applies to normal/attack data
  Find the y-axis ratio of the centroid coordinates
RTT [ms]
Number of packets
Notes: Next, let me explain the detection method. We use the k-means algorithm for detection.
The k-means algorithm is a clustering method that groups data into clusters.
In our case, we use two clusters, and we calculate the y-axis ratio of the coordinates of each cluster's centroid.
This y-axis ratio is then computed separately for the RTT data under normal conditions and the RTT data during an attack.

## Slide 11: Detection method (2)
Calculate y-axis ratio of center of gravity point from normal data ➡ Threshold value
Legal AP
  The y-axis ratio calculated from the normal data
Rougue AP
  The y-axis ratio calculated from the attack data
RTT [ms]
RTT [ms]
Data number
Greater than threshold
➡There is rogue AP
Data number
Notes: Then, for each of the four traffic load conditions, we follow these steps.
The threshold for the y-axis ratio will be determined using one data point from the normal RTT data set.
Then, the y-axis ratio will be calculated for the remaining normal RTT data and the attack RTT data.
By comparing these calculated values with the threshold, if exceed the threshold, it will be concluded that a rogue AP is present.

## Slide 12: Additional detection using CDF
CDF : Cumulative Distribution Function
Additional detection using CDF
  Confidence intervals are constructed and compared to RTT mean
random variable
probability
Normal distribution example
Notes: To prevent false detections, an additional detection method is employed using the cumulative distribution function, commonly known as CDF.
CDF is a function that represents the probability of a random variable being less than or equal to a certain value. In this case, it refers to CDFs that show the probability of taking a value less than or equal to a certain RTT.
Even if the k-means-based detection identifies no rogue AP, when comparing the CDF's confidence interval with the average RTT, if the average RTT falls outside the CDF's range, it is considered as an indication of the presence of a rogue AP.

## Slide 13: Experimental method
Detection with separate traffic load
  Experiments in the 2.4GHz band
  Without Iperf and 3MB, 5MB and 7MB load
IoT
Legal AP
Rogue AP
PC 1
(To measure)
PC 2
Devices
Load using iperf
between PC1 to PC2
Send ping
PC1 to google.com
google.com
Notes: Next, I discuss the experimental setup in more detail.
As mentioned earlier, we conducted the experiments using Iperf between two PCs while sending pings to google.com to measure the RTT until the ping response is received.
During the experiments, the devices connected to the AP included 3 PCs, 1 smartphone, and 16 IoT devices, and the operating frequency was set to 2.4GHz.
We performed the experiments under four traffic load conditions: no Iperf load, Iperf load of 3MB, Iperf load of 5MB, and Iperf load of 7MB.
次に、実験方法について詳しい話をします。 先ほども話した通り、2つのpc間でiperfを使い、その状態でgoogle.comにpingを打ち、pingが返ってくるまでの時間をRTTとして実験をします。 この時、APに接続しているデバイスは、3つのPCと1つのスマートフォン、16個のIoT機器であり、使用している帯域は2.4GHZで行った。 また4つのトラヒックの状態は、iperfなしの状態とiperfで3MBの負荷、5MBの負荷、7MBの負荷の状態の4つである。

## Slide 14: Acquisition Result
Chart: Number of packets
Without iperf, connect with 3 PCs and an iPhone.
Notes: This is the result when done without iperf.

## Slide 15: Acquisition Result
Chart: Number of packets
Load 3MB, connect with 3 PCs and an iPhone.
Notes: This is the result of a 3 MB load on iperf.

## Slide 16: Acquisition Result
Chart: Number of packets
Load 5MB, connect with 3 PCs and an iPhone.
Notes: This is the result of a 5 MB load on iperf.
It can be seen that the dispersion is gradually increasing.

## Slide 17: Acquisition Result
Chart: Number of packets
Load 7MB, connect with 3 PCs and an iPhone.
Notes: This is the result of a 7 MB load on iperf.
Threshold values are set for each of these RTT data for detection.

## Slide 18
Both mean and variance are legal<rogue
RTT increases as load increases
Application of detection programs
Acquisition Result
Witohout Iperf
3MB
5MB
7MB
 | Legal | Rogue
variance | 60.27545 | 558.655
average | 9.761745 | 20.25342
 | Legal | Rogue
variance | 501.2121 | 2105.33
average | 14.47458 | 42.54448
 | Legal | Rogue
variance | 93.30117 | 1533.754
average | 11.2678 | 35.24823
 | Legal | Rogue
variance | 235.8639 | 4069.698
average | 15.34014 | 57.70722
Notes: This is the mean and variance in each pattern.
All means and variances are greater during attacks than during normal times.
And it can be seen that both the mean and variance increase as the load increases.
Detection is carried out on these data as described earlier. The detection results are shown next.

## Slide 19: Detection results (competing method)
F-score : 0.74, Accuracy : 0.79
Only one type of threshold is fixed
  Detection at threshold without Iperf
Without using CDF
 | Not using iperf | Iperf 3MB | Iperf 5MB | Iperf 7MB
Legal | 〇 | 〇 | 〇 | 〇 | 〇 | × | × | 〇 | 〇 | × | × | ×
Rogue | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇
Notes: First, let's start with the results of the competing method.
As mentioned earlier, the competing method uses a single threshold, which is derived from the y-axis ratio calculated from the results when Iperf is not used.
This resulted in an F-score of 0.74 and a percentage of Accuracy of 0.79.
まずは対抗手法の結果からです。 先ほども言ったように、使う閾値は一つのみで、iperfを使用しない時の結果から算出したy軸比を閾値としています。

## Slide 20: Detection results (proposed method)
F-score : 0.92, Accuracy : 0.92
Four measurements with 300 packets per measurement
  1 time used for training data, 3 times for test data
 | Not using iperf | Iperf 3MB | Iperf 5MB | Iperf 7MB
Legal | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | × | 〇 | ×
Rogue | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇 | 〇
Notes: In contrast, the proposed method resulted in an F-score of 0.92 and a percentage of accuracy of 0.92.
The number of RTT data used in one experiment was 300; four measurements were made, one of which was used as the threshold.
１回の実験で使用されたRTTデータ数は300である。4回測定し、そのうち1回を閾値に利用した。

## Slide 21: Summary and tasks
Evil-Twin detection using RTT
  RTT changes depending on traffic load
  Conventional methods may create detection errors
Proposal for a traffic load-aware detection method using the k-means method
Improved F-score compared to not considered
Detection in the 5 GHz band
Notes: In this study, we conducted Evil-Twin detection using RTT. Existing methods often did not consider the impact of traffic load on RTT variations. Therefore, we performed detection with varying thresholds for each traffic load condition. As a result, the F-score and accuracy improved compared to not considering traffic load. For future work, we plan to extend our detection method to the 5GHz band and investigate its effectiveness.
That concludes my presentation. Thank you very much.